## Slide 1: Prehospital sepsis care
Prehospital treatment
Operations
Jason Walchok FP-C
Training Coordinator
Greenville County EMS

## Slide 2: GCEMS Sepsis treatment protocol
Developed in collaboration with the 2 hospital systems in the local area.
Treatment in line with current standard of care for suspected septic patients in hospital.
Process for blood culture collection and appropriate ABX administration.

## Slide 3: Objectives
Review the importance of antibiotic administration for serve sepsis and septic shock.
Describe the importance of blood culture collection prior to antibiotic (ABX) administration.
Understand the need for accurate serum lactate collection
List the steps involved in aseptic blood culture collection
Describe the equipment in the “Sepsis Kit”
Outline the proper steps to antibiotic administration

## Slide 4: Evaluation and Treatment tool
Half sheet (front and back) on Green cardstock for easy recognition in the ED.
Facilitates quick transfer of septic patients in the ED with all pertinent documentation in one place.
  Written and verbal report
  ABX administration time
  Blood collection time

## Slide 5: Evaluation tool
A quick guide for providers during assessment and treatment of a suspected septic patient.
  SIRS criteria
  Common sources of infection

## Slide 6: Treatment tool
Outlines the procedure and treatment methodology for a suspected sepsis patient as outlined in the GCEMS protocol.
  Blood collection
  Fluid administration
  ABX administration

## Slide 7: GCEMS Sepsis treatment steps
Initial assessment and full set of vital signs (including temperature)
Identify suspected septic patient through assessment
  SIRS x2 and known or suspected source of infection
IV access utilizing Chloroprep
  Draw blood cultures
  Draw blood for lactate measurement
Fluid bolus (1000ml NS)
Administer appropriate antibiotic (ABX) IV
Activate “Sepsis Alert”

## Slide 8: GCEMS Training Video
Your equipment and steps may vary depending on your transport destination
This should be used as an example of the GCEMS process for blood collection

## Slide 9: Blood culture collection
Blood cultures are used to detect the presence of bacteria or fungi in the blood, to identify the type present, and to guide treatment.
Collecting blood cultures prior to antibiotic administration offers the best hope of identifying the organism that caused severe sepsis in an individual patient.
This procedure is highly scrutinized in hospital to maintain a low contamination rate.
  Contamination is the presence of an organism in the culture that is not present in the blood. (poor aseptic technique)

## Slide 10: EMS blood culture collection
EMS must beheld to the same standards as the ED for collection.
  Contamination rate <6%
One procedure for all providers to ensure consistency
  Developed in collaboration with receiving hospital systems.
  Your cultures will become their cultures once processed in their lab, hospital labs must maintain a low contamination rate.

## Slide 11: Collection steps
Maintain aseptic technique
  Clean gloves
  Clean area
Scrub the site (AC preferred) with Chloroprep applicator for 30-60 seconds
  2 inches around the site
Allow Chloroprep to dry…. On its own
  “Drying time is dying time”

## Slide 12: Collection steps
Remove caps and clean culture bottles with alcohol
Venipuncture with selected catheter
  Do not touch clean site prior to insertion
Connect vacutainer to the hub of catheter
Fill each blood culture bottle with 5-10 ml blood:
  Aerobic (Blue/Grey) first
  Anaerobic (Purple) second
  If only enough blood is collected for one culture, the Aerobic bottle must be filled before antibiotic administration can be considered.

## Slide 13: Lactate Collection
When oxygen delivery to organs decreases (hypo perfusion) lactate acid is created due to anaerobic metabolism.
This is an indication of organ dysfunction (Severe Sepsis)
If point of care lactate machines are not available, blood for lacate analysis at the ED must be collect by paramedics prior to fluid resuscitation.
It is vital that the initial serum lactate level is known during treatment in hospital.

## Slide 14: Lactate Collection
Either a heparinized blood tube or Grey top blood tube may be used for lactate collection.
  Serum lactate in heparinized blood will only last 20 minutes but can be processed immediately in the ED via and ABG machine.
  Serum lactate in a grey top tube will last 2 hours but will take approx 1 hour to process in the ED laboratory.
Regardless, the initial serum lactate level gives vital information to the receiving physician and critical care team prior to further resuscitation of the patient.

## Slide 15: GCEMS Sepsis Kit
Includes:
  Blood cultures (set)
  Blood tubes (Grey and Green)
  Chloroprep x 2
  Alcohol preps x 2
  Wrist band
  Sepsis assessment and treatment sheet
  Antibiotics and mini-bag

## Slide 16: GCEMS antibiotics
PCN allergy – No ABX (ask specifically)
At least 5cc of blood in the Blue top Culture bottle (Aerobic)
  No Cultures = No ABX
2 SIRS Criteria and known or suspected source of infection.
  “Sepsis Alert”
Administer over 30mins
Administer regardless if a patient is on oral antibiotics.

## Slide 17: Antibiotics
Rocephin (Ceftriaxone)
- 1 Gram
Used in suspected or documented pneumonia only
3rd generation Cephalosporin, broad spectrum activity against gram positive and gram negative pathogens
Inhibits cell wall synthesis

## Slide 18: Antibiotics
Combination antibiotic
  Piperacillin – extended-spectrum penicillin antibiotic
  Tazobactam – b-lactamase inhibitor
Activity against many gram-positive and gram-negative pathogens
Side effect: Relatively safe with no pcn(-cillin) allergies, diarrhea most common.
Indication: All sources of infections other than pneumonia
Zosyn (Piperacillin/Tazobactam )
– 4.5 Grams (OR 3.37 Grams)

## Slide 19: Mini Bag Plus System
Diluent bag with integrated adapter creates an admixture system
Compatible with standard 20 mm closure, single-dose, powdered-drug vials
Can be activated at point of care using proper aseptic technique
No exposed spike or needles
Can be docked outside the pharmacy using proper aseptic technique
Baxter Mini-bag +
50cc NS with vial attachment

## Slide 20: Mini-Bag Plus System
Assembly
1. Remove vial cover
  Disinfect stopper
2. Peel off foil cover
  Inspect adaptor for moisture
  Discard if found
3. Place vial upright
  Hold firmly
  Push adaptor down until vial snaps in place
  DO NOT TWIST
  Pull vial to ensure fully seated

## Slide 21: Mini-Bag Plus System
Reconstitution
4. Squeeze bag and check vial
  Use only if vial fully seated and dry
  Bend up then down to break seal
5. Hold bag with vial down
  Squeeze solution into vial until half full
  Shake to suspend drug in solution
6. Hold bag with vial upside down
  Squeeze bag to force air into vial
  Release to drain suspended drug from vial
  Repeat steps 5 and 6 until vial is empty of drug and solution is thoroughly mixed. Ensure drug is completely dissolved. Do Not Remove Drug Vial.

## Slide 22: Mini-Bag Plus System
Remove port protector.
  Attach administration set per its directions.
8. Hang container on I.V. pole and prime set per directions.
  Ensure that vial is empty of drug and solution. Repeat step 6 if drug and solution remain in vial.
9. Document the time on green sheet and PCR

## Slide 23: Fluid Resuscitation
30ml/kg initial bolus
  1liter followed by a second during extended transports
Observe for signs of fluid overload
  Pulmonary Edema
Consider Dopamine 2-20mcg/kg/min
  After fluid administration and SBP <90mmHg (Septic Shock)

## Slide 24: Reactions
Signs and symptoms of reaction:
  Skin rash
  Hives
  Itching
  Fever
  Swelling
  Shortness of breath
  Wheezing
  Runny nose
  Itchy, watery eyes
  Anaphylaxis
Administration of IV antibiotics does carry the risk of allergic reactions
Be prepared to intervene and immediately stop antibiotic administration of signs of an allergic reaction are observed.

## Slide 25: Data collection
Once the patient is delivered to the ED the Evaluation and treatment tool is filled out and left with the ED staff.
  A copy of the form is set to the training department for QA and data collection.
  ePCR # and crew is collected
  This is compared to contamination records at the ED for identification of providers with deficiencies.

## Slide 26: QA/QI
100% QA on all Sepsis alerts
  Demonstrate the reliability of your assessment tool
Compare Sepsis alerts to in-hospital ICD-9 diagnosis
  Appropriateness of treatment
Provider collecting blood cultures
In-hospital blood lactate levels

## Slide 27: Thank You
Jason Walchok, NRP, FP-C
Greenville County EMS
Training Coordinator
P: 864-467-7389
jwalchok@greenvillecounty.org